## Slide 1
Principles of Underwater sound, December 2016
This class will investigate underwater sound from a computational point of view. We will initially focus on the basic propagation in the ocean wave guide in both frequency and time domain. In the last part of the course will focus on ocean noise and source localization.
Professor Peter Gerstoft, Gerstoft@ucsd.edu Teaching Assistant Jie Li, jil004@ucsd.edu Professor Jiang Zhu
We meet in Zhoushan campus
Main Text: Computational Ocean Acoustics, by Finn Jensen, F.B., Kuperman, W.A., Porter, M.B., Schmidt, H., 2011
Big plan
First class 18 Dec, last 12 Jan.
Computer class Tuesday night and Friday last two classes (bring computer).
Homework due Tuesday 8am and Friday 8am. Email homework/Matlab code to Jie Li, jil004@ucsd.edu
Each week we meet: Tue 8-10:35 Tue 19:20-20:55 computer Thu 14:05-16:40 Fri 14:04-15-40 Fri 15:50-17:30 computer
The first two week focus on ocean wave propagation, Chapter 1-2 and part of 4. Third week on pulse propagation Forth week on beamforming, matched field.

## Slide 2
Classes
week 1:class1: Homework1: read up to page 35. Ask one (any!) question related to this in class. TL (1.3.4), Lloyd mirror (1.4.2), Snells law (check seismics), 1.6 bottom loss
class2 computer homework1
class3 Bottom loss, wave eq., Helmholtz 2-2.3
class4 Layered media 2.4.1- 2.4.2
class5 computer homework2 week 2:
Class6: 2.4.3-2.4
Class7 computer homework3
Class8 ch 4 appendix A
Class9 2.5
Class10 computer homework4 week 3:
Class11: Waveforms COA8.-8.2, 8.3.2, COA 3.2
Class12 computer homework5, FFT
Class13 Seismic waveform reflections, deconvolution
Class14 beamform
Class15 computer homework6 week 4:
Class16: beamform, high resolution beamform
Class17 computer homework7
Class18 Compressed sensing in acoustics
Class19 matched field
Class20 final projects,
week 5 Noise and noise processing. 9.3, 10.4.3

## Slide 3: Practicalities
English
Computer
Homework
Homework2 (Lloyd Mirror to 20km) is due Friday 15,
Homework 3 (problem 1.6 page 62) Tuesday 20
Homework 4 (wavenumber integration) Friday 23
Homework 5 (pulse) Friday 30
Grading, 60%homework, 40% final test
No copying!
Website: noiselab.ucsd.edu/china2017

## Slide 4: Fundamentals of ENVIRONMENTAL OCEAN ACOUSTICS Computational Ocean Acoustics Chapter 1

## Slide 5
SCHEMATIC OF SOUND PROPAGATION PATHS

## Slide 6: What is “Environmental Ocean Acoustics”
Understanding and Modeling the generation and propagation of sound in the ocean
  The ocean is a “thin” sheet with horizontal extend ~ 100 times the vertical, creating a waveguide.
  Sound speed variability
    ~ 10% in vertical
    ~ 1% in horizontal for typical propagation ranges
  Boundary Interaction
    Bottom an “infinite” acoustic and elastic medium
    Ice cover in polar regions
    Surface waves and bubbles
  Signals and noise
  Scattering and Reverberation

## Slide 7
Geometric Spreading
Transmission Loss

## Slide 8
LLOYD MIRROR EFFECT

## Slide 9
Cut and paste from:
Colladen and Sturm
Lake Geneva 1826
“Active Sonar”

## Slide 10
GENERIC SOUND SPEED STRUCTURE

## Slide 11
GLOBAL SOUND SPEED STRUCTURE

## Slide 12: Sound is Attracted to Low Speed of Sound!!
c(z)
Snell’s Law

## Slide 13
Range ~1000 miles
polar latitudes
Mid latitudes
SOSUS array
Typical mid-latitude sound speed profile
Typical northern sound speed profile
Radiated noise
Sea mountain or continental shelf
Ray trapped in the Deep Sound Channel (DSC)
Depth ~10000 ft
Layers of constant sound speed
C (m/s)
Box 1
Historical Underwater Acoustics

## Slide 14
SOUND SPEED, SNELL’S LAW AND ATTENUATION
Snell’s Law
Attenuation
Sound Speed

## Slide 15
DEEP SOUND -CHANNEL PROPAGATION
(NORWEGIAN SEA)

## Slide 16
SURFACE-DUCT PROPAGATION
(NORWEGIAN SEA)

## Slide 17
CONVERGENCE ZONE PROPAGATION
(NORTH ATLANTIC)

## Slide 18
ARCTIC PROPAGATION

## Slide 19
I Presented to here on day 1in China 13 Dec 2016

## Slide 20
SHALLOW WATER SOUND SPEED PROFILES

## Slide 21
REFLECTIVITY

## Slide 22
SHALLOW WATER PROPAGATION

## Slide 23
CONSTRUCTIVE INTERFERENCE
MODAL PROPAGATION

## Slide 24
q1
q2
qn
qc
a)
Box 2
r
z
rb,cb
cw
kr1
kr2
…
krn
b)
Shallow Water Propagation
Ray-Mode Analogy

## Slide 25: Mode Cutoff

## Slide 26
SHALLOW-WATER PROPAGATION
(SUMMER, MEDITERRANEAN)

## Slide 27
CONTOURED PROPAGATION LOSS:
“OPTIMUM FREQUENCY CURVES”
BARENTS
SEA
ENGLISH
CHANNEL

## Slide 28
OPTIMUM FREQUENCY CURVES

## Slide 29: Shallow Water Propagation Modal Interference

## Slide 30: Ocean Seismo-Acoustics
Water
Mud
Silt
Sand
Basalt
Shear Rigidity

## Slide 31: Ocean Seismo-Acoustics Significance
Frequency Environment | ULF < 1 Hz | VLF 1-30 Hz | LF 30-500 Hz | HF >500 Hz
Shallow Water < 300 m | + | + | + | -
Deep Water > 300 m | + | - | - | -
Arctic | + | + | + | +

## Slide 32: Shallow Water Seismo-Acoustics
S
P

## Slide 33: Shallow Water Seismo-Acoustics Scholte Interface Waves

## Slide 34: Arctic Seismo-Acoustics Acoustic Emission from Ice Fractures
Flexural Wave
Longitudinal Wave

## Slide 35
PROPAGATION IN A RANGE DEPENDENT ENVIRONMENT

## Slide 36
PROPAGATION OVER A SEAMOUNT
(NORTH PACIFIC)
data: Chapman and Ebbeson

## Slide 37
HIERARCHY OF UNDERWATER ACOUSTIC MODELS

## Slide 38
MODEL CONSISTENCY
MODES AND RAYS

## Slide 39: 3D Propagation Around Conical Seamount
sound speed profile

## Slide 40: Comparison between 3D and Nx2D solutions
H=1000 m, 3D,
H=1000 m, Nx2D;
H=3800 m, 3D,
H=3800 m, Nx2D.
TL in the horizontal plane at depth 300 m. The source frequency is 10 Hz.

## Slide 41
AMBIENT NOISE SPECTRA
Wenz Curves

## Slide 42
Surface Noise in a Stratified Ocean

## Slide 43
Surface Noise in a Stratified Ocean
Total Field
Continuous
Spectrum
Discrete
Spectrum

## Slide 44: Some Applications

## Slide 45
Sonars

## Slide 46
Underwater acoustic bottom mapping

## Slide 47
Ocean Acoustic Tomography
Different rays have
Different group speeds
Therefore have different
Arrival times
Which ray corresponds
To which arrival time?

## Slide 48: Geo-Acoustic Inversion

## Slide 49
Underwater Acoustic Communication
Transfer Function and Symbol
Spread in Shallow Water
Fo=3500, 1 ms,r=10 km Depth 120m
Fo=6500, .5 ms,r=4km
Depth 50m
Fo=15000, .1 ms,r=.16km
Depth 12m
MUST deal with
Intersymbol Interference
(“ISI”)

## Slide 50
Man Made Sounds
Animal Sounds