## Slide 1: A Robotic Fish Based on Fusion of Visual Image and Ultrasonic Sensor
Presenter: Faizan ur Rehman
Student ID: 21734185
Supervisor: Prof.Dr. Daxiong JI.
Ocean College, Zhejiang University
Thesis-Proposal
December 17, 2018
Notes: We designed this template so that each member of the project team has a set of slides with its own theme where he/she can present their research. Members, here’s how you add a new slide to just your set:
Mark where you want to add the slide: Select an existing one in the Thumbnails pane, click the New Slide button, then choose a layout.
The new slide gets the same theme as the previous one you selected.
Careful! Don’t annoy your fellow presenters by accidentally changing their themes. That can happen if you choose a theme Variant from the Design tab, which changes all of the slides in your presentation to that look.

## Slide 2: Agenda / Topics
Introduction
Motivation
Statement of Problem & Research Question
Objectives
Controller & Sensors
Block Diagram
Prototype Design & Validation test(Terrestrial)
References

## Slide 3: Introduction
An underwater robotic fish which will swims underwater Autonomously.
Able to perfectly identify, classify and detects the objects, obtain quick and proper judgments and decide on the proper path to avoid obstacles.
Autonomously via some inbuilt sensors such as image and distance sensor.

## Slide 4: Motivation
Underwater remotely operated fish
(Zhejiang University)
Underwater target following robotic fish
( Peking University)

## Slide 5: Statement of Problem & Research Question
There is a limited amount of research that has focused on fish robots, especially related to their autonomous behavior or autonomous movements underwater.
How does a fish robot detects and recognize the objects or targets under the water and act autonomously?

## Slide 6: Objectives
Design a underwater robotic fish that can operate autonomously.
To execute autonomous swimming a Pixy CMUcam5 will be installed at the mouth position of robotic fish.
Manoeuvrability will be processed by the embedded microcontroller (Arduino).
Servo motor will use for locomotion of fish.
For obstacle avoidance, Ultrasonic sensor will be utilized.
To observe the underwater circumstances a HD Camera will be installed.

## Slide 7: Controller
Arduino Nano will used as central control board in this project.
Arduino IDE uses C++.
The Arduino assigns commands by "PWM“ a Pulse Width Modulation to the electronic speed controllers that regulate the servo motor.
An emergency stop function will designed to stop the control system.
Arduino Nano

## Slide 8: Servo motor
The aim of Servo motor is to move fish as (Forward, Right & left) direction.
Servo motors allow precise control of its angular position and speed.
A PWM signal is send to control the movement of Servo motor.
HS-646WP Servo Motor

## Slide 9: Image Sensor
Pixy CMUcam5 will used as image sensor to identify the objects
Very fast and efficient image sensor to detect “ hue and saturation” of the image
Memorize up to seven different color signatures
It gives the size, X and Y coordinates of the traced object
Frame rate 50Hz, RAM 264KB and flash memory 1MB
Frame Rate 640X400 pixels
Pixy CMUcam5
Interface Software

## Slide 10: Ultrasonic Sensor
Ultrasonic Sensor JSN-SR04T will used as to avoid the obstacles.
Provide 0.2 m to 4.5 m distance from Ultrasonic module to corresponding object.
Integrated with waterproof probe ended wire.
Trig Pin cause the module to send “Ping” to start browsing.
Echo Pin functioned as the wave is returned after it getting reflected by an object.
Distance= Speed (speed of sound in air/underwater)*Time
JSN-SR04T

## Slide 11: Wireless Charging
An inductive wireless charging module.
It comes with two coils
Transmitter Coil
Receiver Coil
Technology uses magnetic induction to transfer power from a transmitter (Tx) to a receiver (Rx)
The received electrical signal is rectified, filtered and regulated before supplying the load.
12v Wireless Charging Module

## Slide 12: Control System Block Diagram

## Slide 13: Prototype design
The function of the prototype design is to hold the
Pixy CMUcam5
Ultrasonic Sensor
Electronic components
Any weights
For any 3D printed piece, Solid Works was used to create 3D models
3D model of robotic fish
3D Printed robotic fish

## Slide 14: Hydrostatic Pressure
It is the pressure exerted by fluid at any given point within the liquid due to force of gravity. It is increase linearly with the water depth.
According to Pascal’s law;
Where,

## Slide 15: Buoyancy
The robotic fish should be stable and moderately negative buoyant over the pressure to secure a certain depth.
To measure the buoyancy the density and volume of robotic fish are multiplied.

## Slide 16: Validation Test
Initial On Terrestrial Basis

## Slide 17: Autonomous Mode
To examine the auto control, a simplistic task was first created to find a ball based on the hue and saturation of the ball. The algorithm adopted is shown in Figure
If there is no ball then Ultrasonic Sensor will work and servo motor will rotate in forward position if any other object comes in front of Ultrasonic module then servo motor will change it’s position to right.

## Slide 18
Auto Control of Servo motor

## Slide 20: Circuit Diagram

## Slide 21: Project Timeline
MARCH
Design & Construct
APRIL
Circuits Programs
MAY
Testing
Submit paper
December
January
February
March
Design & Construct of Circuit
Installation of Electronic Components
Waterproofing & Testing
Writing Paper

## Slide 22: Conclusion & Future Works
The underwater fish robot is extremely tricky to operate underwater real life situations but works to reveal the concept in a swimming pool well.
The target following and detection technique worked competent using Image sensor and ultrasonic , in future I will work on it more to put PID for the precise autonomous control.
A Computational Fluid Dynamics Analysis will be applied on it.

## Slide 23: References
Zhao, Wei, Yonghui Hu, Guangming Xie, Long Wang, and Yingmin Jia. "Development of vision-based autonomous robotic fish and its application in water-polo-attacking task." In American Control Conference, 2008, pp. 568-573. IEEE, 2008.
Ansari, Muhammad Adil, and Fahim Aziz Umrani. "SONAR based obstacle detection and avoidance algorithm." In Signal Acquisition and Processing, 2009. ICSAP 2009. International Conference on, pp. 98-102. IEEE, 2009.
Hu, Yonghui, Wei Zhao, Long Wang, and Yingmin Jia. "Underwater target following with a vision-based autonomous robotic fish." In American Control Conference, 2009. ACC'09., pp. 5265-5270. IEEE, 2009.
http://www.arduino.cc
http://charmedlabs.com/default/pixy-cmucam5
https://www.kickstarter.com
http://www.bluerobotics.com

## Slide 24
hank
ou!